## Slide 1: Eovsa prototype Performance
Dale E. Gary
Professor, Physics, Center for Solar-Terrestrial Research
New Jersey Institute of Technology

## Slide 2: outline
Purpose of the prototype
Expectations of performance
  Prototype sensitivity
  Prototype stability
Evaluating performance
  Total power checkout
  Phase and amplitude stability (vs. frequency)
  Sensitivity on calibrators (vs. frequency)
  Polarization sensitivity
  Solar performance
Prototype Operation

## Slide 3: purposeS of the prototype
Primary purpose, of course, is to evaluate the performance of the design before building out the remainder of the array.
Secondary purpose is to learn to operate the array
  Use the experience to develop data handling, analysis software, database structure.
  Debug the control system, add features (e.g. subarray control), develop operator display, schedule.
  It is very likely that the correlator will need some redesign/tweaking.
The prototype is also useful for science (but should not distract us)
  Evaluate extent to which we can calibrate the prototype => sensitivity on calibrators.

## Slide 4: Expected Prototype sensitivity
This prototype integrated over a 500 MHz band will be 10 times more sensitive than OVSA was:
  EOVSA Tsys = 560 K, OVSA Tsys = 2000 K
  EOVSA D = 2.1 m, OVSA D = 1.8 m
  EOVSA Dn = 500 MHz, OVSA Dn = 100 MHz
  Expected sensitivity on a baseline is
  so we should expect 10s on 3C84 (~28 Jy) in 25 s. It should be feasible to calibrate 500 MHz bandwidths.
Also have dual polarization, and can flag RFI.
Conclude that sensitivity will permit calibration of individual baselines (baseline determination, amplitude and phase calibration—for 500 MHz bandpass—perhaps even some bandpass calibration).

## Slide 5: Expected prototype stability
Wes has designed an analog system with excellent stability, shooting for 1% in amplitude and 1° in phase.
  The front end includes peltier coolers for temperature stabilization.
  There are no “moving parts” in the front end (for a given attenuator setting), and downconversion occurs in the environmentally stable electronics room.
  Power levels are designed for optimum linearity through the system.
  Power levels are measured in the front end and at the backend prior to downconversion, to ensure correct setting of the front-end attenuation for variable input signals.
These steps in design of the analog system should make the system very stable against temperature and other environmental effects.
We will house the correlator and computers in the electronics room in EMI-shielded racks, which should minimize self-induced RFI.
Our main source of instability will likely be external RFI.

## Slide 6: Evaluating performance
This section assumes we do not have 27-m antennas (yet).
Total power checkout
  Check power levels through system against cascaded noise spreadsheet.
  Check bandpass ripple versus spreadsheet.
  Verify power level and stability over temperature.
  Check linearity for various RFI conditions (i.e. over entire sky).
  Evaluate RFI and create RFI flag table.
  Inter-compare the six TP channels (3 antennas x 2 polarizations).
Cross-correlation checkout
  Phase and amplitude stability vs. frequency, phase closure
    GPS, XM, and Geostationary satellites will give strong, restricted band phases (amplitudes may vary)
    Sun will give strong, all-band phases (but with variable amplitude & phase)
    Will need 3C84 observations to check broadband stability
  Cross-talk (evaluate need for phase switching) – long run on blank sky, look for anomalous correlation
  Evaluate RFI effects, especially weak RFI, over entire sky and on Sun

## Slide 7: Evaluating performance
Sensitivity on Calibrators
  Check quantitative sensitivity on 3C84 vs. integration time
  Check quantitative sensitivity on weaker calibrators and long integrations
  Characterize array parameters (beam efficiency, Tsys, etc., vs. frequency)
Polarization Sensitivity
  Evaluate single-dish cross-talk (geostationary satellites have linear polarization, GPS has RCP—limited frequency range, though).
  Verify correlator digital hybrid (converting linear to circular polarization).
  Evaluate the extent to which cross-talk can be eliminated via adjustment of digital parameters in the correlator.
Solar Performance
  Check on/off Sun power levels and setting of attenuation.
  Check solar increment (on/off Sun) and stability thereof vs. frequency.
  Check pointing performance of each antenna over a full day.

## Slide 8: Prototype operation
Once we have baselines determined, and establish phase and amplitude stability, we can obtain calibration and attempt to operate the array.
There are many benefits to attempting operations besides science:
  Stability of performance: We can determine how stable the system is between calibrations (i.e. how often calibrations are necessary).
  Automation: We can work on the necessary infrastructure to ensure nearly unattended operation. This is essential, since Kjell and Dan will remain very busy and cannot be distracted by daily operations.
  Data handling: We can work on automation of some of the metadata creation (light-curves, spectra) and begin to build the web access to the database.
  Public Relations: It will be good to advertise availability of data, and some science results, to keep the community aware of EOVSA.