## Slide 1: EOVSA Control and monitor System
Gelu M. Nita
NJIT

## Slide 2: EOVSA M&C System
OUTADATED

## Slide 3: Temperature-Controlled Front End Field Module
Noise Diode
Control
Day/Night
Attn. Ctrl.
Solar Burst
Attn. Ctrl.
V/H RF Power Out
Attn. Ctrl.
Temperature Sensors
OUTADATED

## Slide 4: Block Downconvertor Module
V/H Power Out
Freq. Var. Attn. Ctrl
Solar Burst Attn. Ctr.
OUTADATED

## Slide 5: LO Distribution System
Subarray Switch Ctr.
Ping-Pong Switch?
Subarray 2 LO
Ping/Pong LOs
OUTADATED

## Slide 6: Compact Reconfigurable Input/Output (cRIO) Real Time Module: flexible solution for implementing the control/monitor of the EOVSA Antennas
Control and monitor systems of the antenna front end, and the refurbished OVSA antennas motion control system
Automatic NTP server system time synchronization
Dedicated 1PPS SMB input for automatic system clock drift correction
Rugged, embedded control and monitoring system
400 MHz industrial real-time processor for control, data logging, and analysis
128 MB of DRAM for embedded operation
256 MB of nonvolatile memory for data logging
2M gate, 8-slot FPGA chassis for custom I/O timing, control, and processing
-20 to 55 °C operating temperature range
19 to 30 VDC power supply input
RS232 serial port for connection to peripherals
Two 10/100BASE-T Ethernet ports
Full Price: $2800/controller
With Academic Discount: $840/controller

## Slide 7: NI cRIO-9074

## Slide 8: Alternative Controller: NI cRIO-9014 (no FPGA)
Automatic NTP server system time synchronization
Dedicated 1PPS SMB input for automatic system clock drift correction
400 MHz processor
2G nonvolatile storage
128 MB DRAM memory
10/100BASE-T Ethernet port with embedded Web and file servers with remote-panel user interface
Full-speed USB host port for connection to USB flash and memory devices
RS232 serial port for connection to peripherals
dual 9 to 35 VDC supply inputs
-40 to 70 °C operating temperature range
$2,800 Full Price
$2,500 Academic Discount

## Slide 9: NI cRIO-9113: 4-Slot, Virtex-5 LX50 CompactRIO Reconfigurable Chassis
4-slot reconfigurable embedded chassis that will be attached to the cRIO ACC
3M gate Xilinx Virtex-5 reconfigurable I/O (RIO) FPGA core
Ability to automatically synthesize custom control and signal processing circuitry using LabVIEW
DIN-rail mounting options
-40 to 70 °C operating range
$ 1999 Full Price
$ 600 with Academic Discount
cRIO RT Controller+ FPGA Chassis Total Price: $3,100 with Academic Discount

## Slide 10: NI 9403 C Series 32-Ch Bidirectional Digital I/O Module
32-channel digital I/O module for CompactRIO
5 V/TTL, sinking/sourcing digital I/O
Bidirectional, configurable by line
1000 Vrms transient isolation, ±30 V overvoltage protection
Hot-swappable operation
-40 to 70 °C operating range
$340/module

## Slide 11: NI 9205 32-Ch Analog Input Module
32 single-ended or 16 differential analog inputs
16-bit resolution; 250 kS/s aggregate sampling rate
±200 mV, ±1, ±5, and ±10 V programmable input ranges
Hot-swappable operation; overvoltage protection; isolation;
NIST-traceable calibration
-40 to 70 °C operating range
Spring terminal or D-Sub connectivity
$740/module

## Slide 12: NI 9871: 4-Port, RS485/RS422 Serial Interface Module for cRIO
4 RS485/RS422 (TIA/EIA-485/422) ports for CompactRIO
Baud rates from 14 baud to 3.684 Mbaud;
-40 to 70 °C operating range
Data bits: 5, 6, 7, 8; Stop bits: 1, 1.5, 2;
Flow control: XON/OFF, RTS/CTS, None
Individual 64 B UART FIFO buffers per port
Transceiver modes: 4-wire, 2-wire DTR controlled, 2-wire DTR controlled with echo, 2-wire auto
8 to 28 VDC externally powered;
PC-MF4-PT cable included
$470/module

## Slide 13: Motion Control System for the refurbished OVSA antennas (hopefully not needed)
Solution:
NI Soft Motion toolkit in conjunction with cRIO motion control modules ($1300/controller)

## Slide 14: ANTENNA CONTROL COMPUTER NI PXIe-8133 RT 1.73 GHz Intel Core i7-820 Quad-Core With LabVIEW Real-Time
Deployment platform for NI LabVIEW Real-Time
May run in parallel Windows XP Embedded on a dedicated core
2 GB (1 x 2 GB DIMM) dual-channel 1333 MHz DDR3 RAM standard, 4 GB maximum
High-bandwidth PXI Express embedded controller with up to 8 GB/s system and 2 GB/s slot bandwidth
Two 10/100/1000BASE-TX (Gigabit) Ethernet
4 Hi-Speed USB
ExpressCard/34, GPIB, serial, and other
Dedicated 1PPS SMB input for task triggering
$ 6,200 Full Price
$ 5,600 with Academic Discount

## Slide 15: NI PXI-8431/4 (RS485/422) 4-Port Serial Interface for PXI
Compatible with Windows and LabVIEW Real-Time OSs
Minimal CPU overhead with high-speed DMA interface; multicore processor and hyperthreading support
Flexible standard and nonstandard baud rates from 57 baud to 3,000,000 baud
128 B transmit and receive FIFOs
Selectable 4- and 2-wire transceiver modes for full- and half-duplex communication
4 converter cables (10P10C (RJ50) to DB9 male)
$ 617 Full Price
$ 555 with Academic Discount

## Slide 16: CARMA like Architecture
NI-SVE

## Slide 17: Field Point cRIO Controllers
Local MODBUS over TCP/IP communication between the cRIO controller and Antenna Controllers
Local MODBUS over TCP/IP or RS485 communication between the cRIO and a front-end embedded processor used to control/monitor the analog system
cRIO will generate a local 50PPS signal continuously aligned with the distributed 1PPS signal
The local 50PPS trigger will be used to schedule any control task and to fill-in the 50 state frame monitor slots.
The one-second assembled State Sub-Frame will be transmitted via TCP/IP to the ACC on a TBDx50PPS tick following the next 1PPS pulse

## Slide 18: Overview of the EOVSA Control/Monitor Communication Protocols
Antenna Controller: MODBUS over TCP/IP between the Antenna Controller and its Field Point dedicated cRIO-RT Module.
Field Point Modules: TCP/IP between the Antenna Control Computer (ACC) and the field point cRIO-RT modules
LO and DC control systems: MODBUS over RS485 between LO and DC embedded controllers and the ACC system.
ACC to other EOVSA subsystems (e.g. DPP) and observer interface: TCP/IP to read/write the EOVSA state frame as binary stream preceded by a self describing XML template

## Slide 19: Quote for a 15 Antenna minimal(?) configuration

## Slide 20: Potential ACC System Quote