## Slide 1: Front End and Back End analog subsystems
EOVSA Technical Meeting, 6-9 November 2011
W. Grammer, NRAO/NJIT

## Slide 2: OUTLINE
Overview
  System-level diagram
Ambient-Temp Front End (2-meter antenna)
  Apex module
  Control cabinet
Cryogenic Front End (27-meter antenna)
Analog Back End
  Fiber RX and Block Downconverter
  LO generation and distribution
  Mechanical layout

## Slide 3: Analog system overview

## Slide 4: General Characteristics
13 x 2-m + 2 x 27-m antennas
  Ambient-temp. 2-m front end, Tsys < 400K
  Cooled 27-m front ends, Tsys ~ 50K (goal)
  Orthogonal linear polarization outputs
Tunable RF sky frequency range: 1 - 18 GHz
IF baseband output bandwidth: 500 MHz
Full RF BW analog transmission out of antennas, via SM optical fiber, ~ 1.2 km max.

## Slide 5: Feed and front end
Tecom 1-18 GHz Feed

## Slide 6: Power budget in front end
How do we use noise diode cal source? Assume only on blank sky, not during flares.
-35 dBm
-50 dBm
-60 dBm
-70 dBm
0 dBm
-15 dBm
-25 dBm
-35 dBm
-10 dBm
-25 dBm
-35 dBm
-35 dBm
5 dBm
-10 dBm
-20 dBm
-20 dBm
-20 dBm
-20 dBm
-20 dBm
-20 dBm
+7 dBm
+7 dBm
+7 dBm
+7 dBm
35 dB
~15 dB
0/10 dB
0-25 dB
~27 dB
f -switch inversion?

## Slide 7: Front end component selection
System-level considerations
  Dynamic range
  High linearity
    Requirement driven by RFI levels, detection limit
  Min. gain ripple/slope, any 500 MHz segment
    Depends on quantization level in Correlator?
  Low gain and phase drift (small TC)
    May require temp. control; one-sided (no TECs)?
  Reliability
    Elevated temp. environment (> 40 ºC); lightning protection ?

## Slide 8: Front End Component selection
LNA
  For Tsys < 400K, NF ~ 2 dB may be OK, if feed loss < 1.5 dB across band
  Possible sources: Caltech, Microsemi, others ?
2nd/3rd Stage Amps
  Need additional gain to compensate for loss of added output pads (for LF stability), and min. loss of filter, attenuators
  Low Tc of gain desired – may require eval. testing
  Could use a VGA for 2nd or 3rd stage, if available
  Possible sources: PMI, Miteq, Microsemi, Hittite, Marki, AMI

## Slide 9: Front End Component selection
Digital RF Attenuators
  Step resolution: 1 dB is sufficient
  Phase change w/atten. set is not an issue – calibrated out
  Possible sources: Narda, JFW, Herley, Hittite
Couplers/Splitters
  Possible sources: Narda, MCLI, M/A-Com?
1-18 GHz Lowpass Filter
  Rejects RF signals at 20-20.5 GHz from leaking through
  Possible sources: K&L
Noise Diode
  Possible sources: Noise-Com

## Slide 10: Front end module - mechanical
Envelope is a 12” dia. cylinder (or ~ 8.5” x 8.5” rectangular box), TBD length
Weight limit is 20 lbs., pref. center of mass close to mounting plate
Component layout and packaging a challenge:
  Some components (e.g., couplers) are quite long
  Heat-generating components within a sealed outdoor box make thermal management difficult
  Recommend thermal modeling – NRAO has software (?)

## Slide 11: Problematic In-band rfi at site
Known strong fixed source at ~1.95 GHz
  May require a notch filter after LNA or 2nd stage amplifier, with >20 dB rejection
  Passive notch filter properties
    Need very high Q for a sharp, narrow-band response, combined with flat passband to 18 GHz.
    May be difficult to design, as it also has to be compact
  Interference cancellation could be an elegant alternative, but may add complexity and cost
  Need to research both, determine which is viable

## Slide 12: Antenna control cabinet
Primarily for vendor-equipped motor controllers, power distribution for 2-m antenna
Space was provided for cRIO M&C unit, not much else
Addition items for installation at each antenna:
  Fiber breakout box, 6 conn. ports + 1 duplex cable
  Ethernet switch (1 x optical, ~4 x RJ-45)
  Optical demodulator for 1PPS timing signal
  Front End temperature control electronics
  Power supplies for Front End and all the above
May want a 2nd cabinet for above items.
  Can easily be located on same stand as existing box, or back-to-back.

## Slide 13: Photo of antenna cabinet

## Slide 14: Ant. Cabinet component selection
Fiber breakout box
  Details TBD
Ethernet switch
  Min. (4) Cat5 + full duplex SM opt., 10/100 Mbps
  1310 nm wavelength chosen; use same at other end
  Extended temp. range (-20 to 70°C); high MTBF
  Possible sources: Moxa, Phoenix Contact, Black Box, TC Communications)
  Moxa unit is very competitively priced (~$400), rugged, and has EMI and other certifications.

## Slide 15: Ant. Cabinet component selection
Optical RX/Demodulator for 1PPS, timing
  How are they generated optically? BPSK or AM-modulated RF subcarriers over fiber?
  COTS product or custom design, depending on reqs.
  Should be fairly compact, low-power, robust
  Other requirements?
Front End temperature control
  Heat-only is simpler, more reliable, BUT only if OK to run at elev. temps (~50-55°C).. Can use PWM AC – no DC supply.
  TEC requires hefty low-voltage DC supply, external heatsink, fans. Reliability a concern.
  cRIO can be used for M&C, or separate COTS controller (remoted)
  Mechanical thermal cutoff switch on heaters (Klixon), for safety

## Slide 16: Ant. Cabinet component selection
Pointing telescope controller?
  Is a temporary installation for a one-off measurement – do not need to support this
Power supplies
  Recommend linear supplies for Front End module electronics, to avoid risk of spurious switching noise modulation on output signals
  Switching supplies can be used for everything else
  Recommend adding diagnostic M&C points for all supply outputs (voltage and currents)

## Slide 17: Analog downconversion

## Slide 18: Power budget in back end
-35 dBm
-35dBm
-35 dBm
-35 dBm
-5 dBm
-5 dBm
-5 dBm
-5 dBm
30 dB
-15 dBm
-30 dBm
-5 dBm
-15 dBm
-15 dBm
-15 dBm
solar + band variation
solar variation
-5 dBm
-5 dBm

## Slide 19: Back end component selection
Important considerations
  Good dynamic range
  High linearity (for in-band RFI)
  Minimal passband gain ripple
  Highly stable gain/phase with temperature
  High spurious and image rejection

## Slide 20: back End Component selection
Amplifiers
  Need somewhat more overall gain, to compensate for addl. fixed pads on mixer and filter ports
  Low Tc of gain desired – may require eval. testing
  Could use VGA(s) w/integrated digital attenuator
  Possible sources:
    (RF): PMI, Miteq, Microsemi, Hittite
    (IF): M/A-Com, Mini-Circuits, PMI, Hittite, Microsemi, RFMD, Analog Devices
    (LO): Hittite, Marki, Microsemi, PMI
  May need isolator on LO amplifier inputs, to reduce LO output ripple
Equalizer
  Active “cable amp” with positive gain vs. freq. slope, compensates for negative slope from cables over ultra-wide 1-18 GHz band
  Sources: PMI

## Slide 21: back End Component selection
Digital RF Attenuators
  Step resolution: 1 dB is sufficient
  Phase change w/atten. setting a concern?
  Possible sources: Narda, JFW, Herley, Hittite, Mini-Circuits
Mixers
  Ultra-wide bandwidths might require triple-balanced design, for adequate higher-order rejection (TBC).
  Minor downside of this is higher LO power requirement
  Possible sources: Marki, Miteq, Hittite ?, M/A-Com ?
Microwave (1st IF) bandpass filter
  Small fractional bandwidth (~2.5%) makes it more difficult to get sharp passband response. A cavity filter design might work well here.
  What level of LO and spurious rejection is required?
  Possible sources: K&L, Narda?, MCLI?

## Slide 22: LO distribution system

## Slide 23: LO distribution component selection
Hittite HMC-T2240 Synthesizer selected for LO1
  Broad tuning range: 10 MHz – 40 GHz, 1 Hz resolution
  +20 dBm min. output over LO1 tuning range
  -52 dBc spurious subharmonics over LO1 tuning range, +10 dBm output
  SSB phase noise (dBc/Hz @ f_offs), fo = 30 GHz:
    -50 @ 10 Hz; -83 @ 1 kHz; -87 @ 100 kHz
    -106 @ 1 MHz; -128 @ 10 MHz; < -140 dBc/Hz n.f.
  10 MHz int/ext ref.; < 1 ppm/yr. drift, 1.5 ppm acc.
  500 us freq. sw. time; not freq-agile
  Manual or remote control via USB, GPIB or Ethernet
  Dual-unit rack mount kit available

## Slide 24: Hittite hmc-t2240 Synthesizer

## Slide 25: LO distribution component selection
Fixed-tuned LO2 synthesizer (21.15 GHz)
  Comparable phase noise, spurious specs to LO1
  Assume +20 dBm minimum output (TBC)
  Internal ref. not needed – locked to LO1 10 MHz reference output (+10 dBm available)
  Compact box module w/ext. DC supply preferred, mounted close to 16-way splitter
  M&C functions: Lock and Alarm outputs, output power monitor
  Possible sources: Miteq, Frequency Sources ?

## Slide 26: Lo distribution component selection
16-way Power Dividers
  Possible sources: MCLI
  Coupled RF detector on one output, remotely monitored
Cabling
  2.9mm coax required for single-mode operation to 40 GHz on LO1 lines.
    Higher unit loss than .141 semi-rigid SMA
    More costly
  Recommend same for LO2 lines
  Length matching LO dist. cables on each subarray?
    Greatly reduce differential phase drift over temperature
    Need to check cable properties to quantify this effect

## Slide 27: LO Distribution component selection
Suggest a non-reflective SP2T switch, if available
  Reflections from unterminated switch ports degrade isolation between the splitter ports
  Will reduce power reflected back into LO source
Consider using a mechanical coaxial switch
  Much higher isolation, w/lower VSWR and insertion loss
  100ms switching time, cycle life OK in this case (unless we opt for “ping-pong” LO1 A-B switching, to get around limitations of Hittite LO1 source).
  Single DC supply, low power (if latching)
  Possible candidate: Dow-Key 521Y series

## Slide 28: Back End Power, M&C, packaging
Recommend linear DC supplies for analog components in signal path, for same reasons as in Front End
Rack-level monitor and control unit will be cRIO
Co-locate LO distribution network in the same rack, close to Downconverter modules, to keep cable lengths as short as possible
Lay out modules for flow-through cooling? More constrained, but more uniform temperature distribution across modules.

## Slide 29: General questions & comments
Does construction budget include component spares? What level? (Ans: unknown)
What is the expected operational life of EOVSA? (Ans: assume 5 years, but could be longer)
Subsystem documentation standards? (Ans: None at the moment)