## Slide 1: Digital FX Correlator
Nimish Sane
Center for Solar-Terrestrial Research
New Jersey Institute of Technology, Newark, NJ
EOVSA Preliminary Design Review
March 15-17, 2012

## Slide 2: Overview
No. of antennas | 16
No. of polarizations | 2
No. of frequency channels (subbands) | 4096
Integration time (ms) | 20 (possibly, tunable)
IF (MHz) | 600
ADC
F-Engine
X-Engine
P, P2
Calculation

## Slide 3: Hardware
KatADC
Roach-2 board [1]
  Virtex-6 SX475T FPGA (XC6VSX475T-1FFG1759C)
  PowerPC 440EPx stand-alone processor to provide control functions
  2 x Multi-gigabit transceiver break out card slots, supporting up to 8x10Ge links which may be CX4 or SFP+
8 boards with 2 antennas (dual-polarization) per board

## Slide 4: KatADC
Hardware
  20dB Gain Block (50.0MHz - 850.0MHz) [RF front-end can be upgraded with a higher frequency device (SBB-5089Z: 50.0MHz - 6.0GHz)]
  0dB to 31.5dB Variable Attenuator (controllable in 0.5dB steps)
  Non-reflective 50ohm RF switch to disconnect input
  Provision for a fixed attenuator (LAT-series)
Software Library (“Yellow Block”)
  Available from SKA, South Africa group
  Not clear how to control attenuation and enable inputs (problems when using software registers as inputs to this yellow block)

## Slide 5: F-Engine
Coarse delay: The maximum value supported should be actually 12000 ADC samples (corresponding to 10000ns)
For polarimetry: We will need values for each frequency channel for each sky frequency band (34 x 4096)
While converting to circular polarization, the factor of 1/sqrt(2) has not been included. This is taken care of by diving the result of P or X-correlation by 2 (right shift by 1 bit in digital hardware). This results in 5-bit output in case circular polarization is used. When using linear polarization, the MSB is always zero.
ADC
Phase
Switching
Coarse Delay
PFB
FFT
(4096 channels)
Polarimetry
Linear/Circular Polarization*
Power (P),
P^2
gx, gy, Dx, Dy
Quantization to 5 bits*
To X-engine
Phase
Switching
Pattern
delay
[0, 10000]
To DPP

## Slide 6: F-Engine Comments
We decided not to do fine delay correction in the correlator.
Data rates:
  No. of F-engines per Roach board = 4 (2 antennas dual polarization)
  P (32-bit): Data rate: 32 * 4096 * 50 * 4 bits/sec
  P2 (64-bit): Data rate: 64 * 4096 * 50 * 4 bits/sec
  Total data rate per Roach board (F-Engine to DPP): 96 * 4096 * 50 * 4 ≈ 78.6 Mbps
  Data from F-engine to X-engine per Roach board = 20 x 4 bits/clock cycle = 24 Gbps
At what point do we throw 100 MHz? (≈ 672 channels) --- For now, in DPP/ downstream of Correlator

## Slide 7: F-Engine: Current Status
ADC
Phase
Switching
Coarse Delay
PFB
FFT
(4096 channels)
Polarimetry
Linear/Circular Polarization*
Power (P),
P^2
gx, gy, Dx, Dy
Quantization to 5 bits*
To X-engine
Phase
Switching
Pattern
delay
[0, 10000]
To DPP
FPGA Resource | Utilization (%)
Occupied slices | 20
BRAM (36 x 36) | 16
BRAM (18 x 18) | 12
DSP48E1s | 28
Slice LUTs | 19
Slice registers | 11
FPGA Clock frequency of 150 MHz

## Slide 8: F-Engine: Issues
Hardware
  KatADC hardware upgrade
Software/Implementation
  KatADC software library block and control
  Compiling design at 300 MHz FPGA clock
  Compiling the design with scheme to have 34 x 4096 values of each of the coefficients required for polarimetry
Synchronization/Timing
Power calculation and feedback to ADC
Data transfer to X-engine and DPP

## Slide 9: X-Engine
XA
YA
XB
YB
Xtest
Ytest
.
.
.
XAXB
YAYB
XAYB
YAXB
XAX1
YAY1
XAY1
YAX1
XBXtest
YBYtest
XBYtest
YBXtest
.
.
.
X1X2
Y1Y2
X13Xtest
Y13Ytest
.
.
.
Y1Y3
X1X3
Visibility 0
Visibility 28
Visibility 1
.
.
.
Visibility 29
Visibility 119
Visibility 30
.
.
.
.
.
.
.
.
.
Baselines that include at least one 27-m antenna
(Antenna # A and Antenna # B)
EOVSA Design
Each X-engine (one per each Roach board) processes 4096/8 = 512 spectral channels.
X1
Y1

## Slide 10
X0
Y0
X1
Y1
X3
Y3
X0X1
Y0Y1
X0Y1
Y0X1
X0X2
Y0Y2
X0Y2
Y0X2
X0X3
Y0Y3
X0Y3
Y0X3
X2X3
Y2Y3
Visibility 0
Visibility 2
Visibility 1
Visibility 5
Baselines that can include at least one 27-m antenna
(Antenna # 0 and Antenna # 1)
EOVSA
4-antenna Prototype Design
X2
Y2
Y1Y2
X1Y2
Y1X2
Visibility 3
Y1Y3
X1Y3
Y1X3
Visibility 4
X1X2
X1X3
Each X-engine (one per each Roach board) processes 4096/2 = 2048 spectral channels.
X-Engine

## Slide 11: X-Engine
Each X-engine will handle 4096/8 = 512 frequency channels (256 even and 256 odd channels)
Each input (X or Y) is Fix 5_3
Output of multiplication (and division by 2 if converted to circular polarization) is a Fix 10_3 real part and Fix 10_3 imaginary part
Accumulating with maximum accumulation length of 2^16, the output of vector accumulator is a Fix 26_6 real part and Fix 26_6 imaginary part
Each output (XX, YY, XY, YX) is Fix 26_6 * 2 (real and imaginary) * 2 (odd and even channel) = 104 bits
X0
Y0
X1
Y1
X0X1
Y0Y1
X0Y1
Y0X1
Complex Multiplication
Vector Accumulation

## Slide 12: X-Engine: Comments
X-Engine Output | 4-antenna prototype | EOVSA design (16-antenna)
Visibilities with XX, YY, XY, and YX outputs | 5 | 29
Data per accumulation (bits) | 104 * 4 * 5 * 1024 = 2080 K | 104 * 4 * 29 * 256 = 3016 K
Visibilities with XX, and YY outputs only | 1 | 91
Data per accumulation (bits) | 104 * 2 * 1 * 1024 = 208 K | 104 * 2 * 91 * 256 = 4732 K
Total data per accumulation (bits) | 2288 K | 7748 K
Total data rate (Mbps) (20 ms accumulation time) | 114.4 | 387.4

## Slide 13: X-Engine: Current Status
X0
Y0
X1
Y1
X3
Y3
X0X1
Y0Y1
X0Y1
Y0X1
X0X2
Y0Y2
X0Y2
Y0X2
X0X3
Y0Y3
X0Y3
Y0X3
X2X3
Y2Y3
EOVSA
4-antenna Prototype Design
X2
Y2
Y1Y2
X1Y2
Y1X2
Y1Y3
X1Y3
Y1X3
X1X2
X1X3
FPGA Resource | Utilization (%)
Occupied slices | 4
BRAM (36 x 36) | 8
BRAM (18 x 18) | 0
DSP48E1s | 2
Slice LUTs | 4
Slice registers | 1
FPGA Clock frequency of 150 MHz

## Slide 14: X-Engine: Issues
Software/Implementation
  X-Engine with 120 visibilities has been implemented, but it did not compile successfully
  Compiling design at 300 MHz FPGA clock
Data transfer from X-engine to DPP

## Slide 15: F and X-engine Connections
For prototype, we should be able to fit both F and X engines on the same Roach board
For the final design – we will have to check availability of BRAM resources (more work is needed to come to a conclusion)
Use full-duplex bidirectional capacity of 10 GbE link: Send output of F – engine to a switch that will distribute it to X – engines (even if F and X are on the same board)
All Roach boards have identical design

## Slide 16: F-X-DPP Interconnection
F
P
Q
DPP
114.4 Mbps
114.4 Mbps
78.6 Mbps
78.6 Mbps
EOVSA
4-antenna Prototype Design
6 Gbps
6 Gbps
6 Gbps
6 Gbps
F
Q
P
X
X
10 GbE port

## Slide 17: F-X-DPP Interconnections: Possible Variations
F
P
Q
DPP
114.4 Mbps
114.4 Mbps
78.6 Mbps
78.6 Mbps
6 Gbps
6 Gbps
6 Gbps
6 Gbps
F
Q
P
X
X
293 Mbps
293 Mbps
10 GbE port
1 GbE Link
1 GbE Link
Switch
EOVSA
4-antenna Prototype Design

## Slide 18: F-X-DPP Interconnection
DPP
EOVSA
Design
Switch
F0
F2
F3
F4
F1
F5
F6
F7
X0
X2
X3
X4
X1
X5
X6
X7

## Slide 19: F – X Packets
F to X: Each port sends 1024 channels in a single 4096-channel frame
  Accumulation length = No. of data frames per accumulation = 2930
  6 frames per packet
  No. of packets/acc = 2930 / 6 = 488.33
# of packets in an accumulation can exceed 256 (but does not affect DPP)
All packets may not have same number of frequency channels (but does not affect DPP)

## Slide 20
P to DPP (2 antenna dual polarization)
  No. of bytes per accumulation = 96 * 4096 * 4 / 8 = 192 K
  A possible packet size: 6 KB
  # packets/accumulation = 32
  # of frequency channels / packet = 4096 / 32 = 128
X to DPP
F/X-DPP Packets
EOVSA
4-antenna Prototype Design
Output precision for XX/YY/XY/YX | Fix 26_6 | Fix 24_4 | Fix 24_4 | Fix 22_6 | Fix 32_6
Accumulation size (KB) | 286 | 264 | 264 | 242 | 352
Possible packet size (KB) | 6 | 6 | 4.125 | 7.5625 | 5.5
# packets/accumulation | 47.67 | 44 | 64 | 32 | 64
# Frequency channels/packet | 85.92 | 93.09 | 64 | 128 | 64

## Slide 21: F-X-DPP Interconnections Issues
Architecture
Use of 1 GbE vs 10 GbE ports
Size of a Switch and choice of Switch
DPP input ports
Collision while sending data to the same DPP input port

## Slide 22: 10 GbE Packet Header
Header in a packet should include
  Header length (1 byte)
  Accumulation length (2 bytes)
  Packet number within an accumulation (1 byte)
  Accumulation number (global) (4 bytes)
  Accumulation number (within 0 and 49) (4 bytes)
    This is used to align with the 1 pps signal
  Delay0, Delay1, Delay2, Delay 3 (4 bytes each)
  FFT Shift (4 bytes)
  ADC overflow count (4 bytes)
  For P/P^2
    Antenna number (1 byte)
    Polarization (X, Y, R, L) (1 byte)
  For X-engine output,
    Visibility (2 bytes: 1 byte for each antenna number)
    Roach board number or Engine number (1 byte)
  Whether it is P/P^2 information or X-corr information (1 byte) (?)
  ?
A length of 40 bytes should suffice

## Slide 23: Miscellaneous Issues
What happens when a signal exceeds the 4-bit quantization?
  Data is lost.
  Dale: We may be better off scaling for 3 bits and leaving at least 1 bit of headroom. At least the Van Vleck correction can apply to fewer bits, and while we lose efficiency we do not lose the data itself.

## Slide 24: References
https://casper.berkeley.edu/wiki/ROACH2
P. McMahon, et al. “CASPER Memo 017: Packetized FX Correlator Architectures,” September 2007.