## Slide 1: Digital System Review and Status
Nimish Sane
Center for Solar-Terrestrial Research
New Jersey Institute of Technology, Newark, NJ
EOVSA Prototype Review
September 24-26, 2012

## Slide 2: EOVSA

## Slide 3: Correlator Specifications
No. of antennas | 16 (27-m x2 + 2-m x13 + 1 test input)
No. of polarizations | 2
No. of frequency channels (subbands) | 4096
Spectral resolution* | 122 kHz/channel
Integration time (ms) | 20 (possibly, tunable)
Bandwidth (MHz) | 600
Simultaneous observations in both right-circular (RCP) and left-circular (LCP) polarizations | 
The number of frequencies will be reduced to science resolution (varying between 1 and 50 MHz over the 18 GHz range) after flagging RFI | 
* ~140000 frequencies from 1-18 GHz | 

## Slide 4: Hardware
ADC (x4, x16)
  KATADC
  2 per ROACH-2 Board; each KATADC handles 2 inputs
Roach-2 board (x2, x8)
  Virtex-6 SX475T FPGA (XC6VSX475T-1FFG1759C)
  PowerPC 440EPx stand-alone processor to provide control functions
  2 x Multi-gigabit transceiver break out card slots, supporting up to 8 x 10Ge SFP+ links or 6 x 10Ge CX4 links
8 boards with 2 antennas (dual-polarization) per board
Network switch
  Prototype: 10-port CX4
  Final design: >34 ports, mostly SFP+

## Slide 5: KatADC
Hardware
  RF front-end upgraded with higher frequency device (SBB-5089Z: 50.0 MHz – 6.0 GHz)
  20dB Gain Block
  0dB to 31.5dB Variable Attenuator (controllable in 0.5dB steps)
  We find that it takes around 1.5 ms for the change in attenuation to take effect. However, the settling time is roughly around 0.02 ms. Hence, we may decide to use these features in future versions.
Software Library (“Yellow Block”)
  mlib_devel from the SKA, South Africa github branch

## Slide 6: F-Engine
ADC
Phase
Switching
Coarse Delay
PFB
FFT
Polari-metry
P, P2 + VACC
To DPP
4-bit Quantization
To X-engine
gx, gy, Dx, Dy
Phase
Switching
Pattern
delay
[0, 12000]
Ax
Ay
ADC
Phase
Switching
Coarse Delay
PFB
FFT
Polari-metry
P, P2 + VACC
To DPP
Bx
By
4-bit Quantization
To X-engine
gx, gy, Dx, Dy
Phase
Switching
Pattern
delay
[0, 12000]
~ 10000 ns
Walsh Sequence
4096 Channels
Using full precision output of FFT; Used for spectral kurtosis for RFI excision

## Slide 7: F-Engine: Polarimetry
gx, gy, Dx, Dy
Generate per-channel values
(34 x 4096 values)
Computation
Convert to Circular Polarization
MUX
Select polarization
Down-stream
DSP
Calibration and polarimetry paramters
(34 x 64 values)
Linear Interpolation
FFT Output
Y’
X’
Y
X
L
R

## Slide 8: F-Engine Data Rates
Each ROACH 2 board will have 4 inputs (2 antennas dual polarization)
Assuming integration (accumulation) time of 20ms (50 accumulations/s)
Power (32-bit) Data rate: 32 * 4096 * 50 * 4 bps
Power2 (64-bit): Data rate: 64 * 4096 * 50 * 4 bps
Total data rate per Roach board (F-Engine to DPP): 96 * 4096 * 50 * 4 ≈ 78.6 Mbps
Data from F-engine to X-engine per Roach board = 16 x 4 bits/clock cycle = 19.2 Gbps (@ 300MHz FPGA clock)

## Slide 9: F-Engine: Current Status
FPGA Resource | Utilization (%)
Occupied slices | 23
BRAM (36 x 36) | 15
BRAM (18 x 18) | 12
DSP48E1s | 29
Slice LUTs | 21
Slice registers | 12
FPGA Clock frequency of 150 MHz
ADC
Phase
Switching
Coarse Delay
PFB
FFT
Polari-metry
Power (P),
P^2
To DPP
4-bit Quantization
To X-engine
gx, gy, Dx, Dy
Phase
Switching
Pattern
delay
[0, 12000]
Ax
Ay
Compiling design at 300 MHz FPGA clock
Data transfer to X-engine and DPP

## Slide 10: X-Engine
XA
YA
XB
YB
Xtest
Ytest
.
.
.
XAXB
YAYB
XAYB
YAXB
XAX1
YAY1
XAY1
YAX1
XBXtest
YBYtest
XBYtest
YBXtest
.
.
.
X1X2
Y1Y2
X13Xtest
Y13Ytest
.
.
.
Y1Y3
X1X3
Visibility 0
Visibility 28
Visibility 1
.
.
.
Visibility 29
Visibility 119
Visibility 30
.
.
.
.
.
.
.
.
.
Baselines that include at least one 27-m antenna
(Antenna # A and Antenna # B)
EOVSA Design
Each X-engine (one per each Roach board) processes 4096/8 = 512 spectral channels.
X1
Y1

## Slide 11
X0
Y0
X1
Y1
X3
Y3
X0X1
Y0Y1
X0Y1
Y0X1
X0X2
Y0Y2
X0Y2
Y0X2
X0X3
Y0Y3
X0Y3
Y0X3
X2X3
Y2Y3
Visibility 0
Visibility 2
Visibility 1
Visibility 5
Baselines that can include at least one 27-m antenna
(Antenna # 0 and Antenna # 1)
X2
Y2
Y1Y2
X1Y2
Y1X2
Visibility 3
Y1Y3
X1Y3
Y1X3
Visibility 4
X1X2
X1X3
Each X-engine (one per each Roach board) processes 4096/2 = 2048 spectral channels.
X-Engine
EOVSA
4-antenna Prototype Design
Using CASPER library x engine block

## Slide 12: X-Engine: Data rates
X-Engine Output | 4-antenna prototype | EOVSA design (16-antenna)
Visibilities | 6 | 120
Output per visibility (bits) | 20 bits per output * 4 outputs * 2 for complex numbers = 160 | 20 bits per output * 4 outputs * 2 for complex numbers = 160
No. of channels/x-engine | 2048 | 512
Data per accumulation | 160 * 2048 * 6 = 1920 kb | 160 * 512 * 120 = 9600 kb
Total data rate (Mbps) (20 ms accumulation time) | 93.75 | 468.75

## Slide 13: F-X-DPP Interconnection
DPP
EOVSA
Design
Switch
F0
F2
F3
F4
F1
F5
F6
F7
X0
X2
X3
X4
X1
X5
X6
X7
F and X engines on the same Roach board
Use full-duplex bidirectional capacity of 10 GbE link:
  Send output of F – engine to a switch that will distribute it to X – engines (even if F and X are on the same board)
All Roach boards have identical design
(P. McMahon, et al. “CASPER Memo 017: Packetized FX Correlator Architectures,” September 2007)

## Slide 14: F-X-DPP Interconnection
F
P
Q
DPP
< 100 Mbps
< 100 Mbps
< 100 Mbps
< 100 Mbps
EOVSA
4-antenna Prototype Design
< 10 Gbps
< 10 Gbps
F
Q
P
X
X
Final design
< 500 Mbps
Final design
< 500 Mbps

## Slide 15: F-X-DPP Interconnection
F
P
Q
DPP
EOVSA
4-antenna Prototype Design
F
Q
P
X
X
10 GbE port (CX4 connection)
10 port Switch

## Slide 16: Status
Linear interpolation for polarimetry
Compute P, P^2 in time domain
Choice of 10 GbE/1 GbE
Data rate calculations
Coarse delay (value, changing with 1 pps)
KATADC control & attenuation
Conversion to Circular polarization (Factor 2^(1/2))
Collision
Switch
Byte swap little/big endien
Accumulation length calculation
F to X and X to DPP data packaging + Header

## Slide 17: Status
F-engine is complete except packetizing data to be sent to X-engine
X-engine is in progress
10-port CX4 switch is yet to identified
Testing is going to be the most critical component
Roach2 boards should be with us in 2 weeks